TG68-BASED EXPERIMENTAL SOC
REGISTER DOCUMENTATION

VIDEO CONTROLLER
Base address 0x800000

FRAMEBUFFER

0	Long	Framebuffer address

4	Word	Even row modulo (not yet implemented)

6	Word	Odd row modulo (not yet implemented)

8	Word	HTotal - the total number of pixel clocks in a scanline (not yet implemented)

A	Word	HSize – number of horizontal pixels displayed (not yet implemented)

C	Word	HBStart – start of the horizontal blank (not yet implemented)

E	Word	HBStop – end of the horizontal blanking period. (Not yet implemented)

10	Word	Vtotal – the number of scanlines in a frame (not yet implemented)

12	Word	Vsize – the number of displayed scanlines (not yet implemented)

14	Word	Vbstart – start of the vertical blanking period (not yet implemented)

16	Word	Vbstop – end of the vertical blanking period (not yet implemented)

18	Word	Control (not yet implemented)
bit 7	Character overlay on/off (not yet implemented)
bit 1	resolution – 1: high, 0: low (not yet implemented)
bit 0	visible. (not yet implemented)

Interrupts: Int 1 - vblank

SPRITE

100	Long	Sprite 0 pointer. Sprite is 16 pixels square, in 4-bit “truecolour” format.
Bit 0: opacity, 1: red, 2: green, 3: blue

104	Word	Sp0XPos

106	Word	Sp0YPos

CHARACTER BUFFER
used for the character overlay:
Base address: 0x800800 – 0x800fff, 2048 bytes.

PERIPHERAL CONTROLLER
Base Address 0x810000

UART

0	Word	UART IO
Read
bits 15 downto 11 – don't care
bit 10	txint – a TX int has occurred since the last read. Cleared on read
bit 9	rxint – an RX int has occurred since the last read. Cleared on read
bit 8	txready – previously submitted data has been transmitted.
Bits 7 downto 0 – received data
Write
Bits	15 downto 8 – don't care
Bits	7 downto 0 – data to be sent.

2	Word	UART_CLKDIV – clock divisor for the baud rate generator.
For a 112.5 MHz sysclk, 115,200 baud, use 112,500,000 / 115,200 = 976 (0x3d0)

Interrupts: Int 2 – byte sent / received

MISC

4	Word	Flags – not yet fully defined
Read
Bit 0 – ROM overlay.
Bits 15 downto 6 – switch status. (DE1 only?)
Write
Bit 0 - ROM overlay. When 1, reads to the lower 64k will come from
the M4K-based BootROM. Writes still go to RAM.

6	Word	Hex display – writes are currently routed to the DE1 board's hex display.
On the C3 board, they're sent to the power LEDs, until I define a
proper register for those.

KEYBOARD / MOUSE

8	Word	PS/2 Keyboard
A	Word	PS/2 Mouse
Read
Bits 15 downto 12 – don't care
Bit 11	Data received flag. Cleared on read.
Bit 10	Ready to send. Zero while a byte is being sent to the PS/2 device
Bits 9 downto 0 – stop bit, parity bit, then 8 data bits.
Write
Bits 15 downto 8 – don't care
Bits 7 downto 0 – byte to be sent to PS/2 device

Interrupts: Int 4 – data sent / received

TIMERS:

E	Timer Control word
Read
Bits 15 downto 6, 1 don't care
Bit 5	tr5 – set by timer event, cleared on read.
Bit 4	tr4 – set by timer event, cleared on read.
Bit 3	tr3 – set by timer event, cleared on read.
Bit 1	tr2 – set by timer event, cleared on read.
Bit 2	tr1 – set by timer event, cleared on read.
Write
Bits 15 downto 4, 8 downto 0 – don't care
Bit 13	en5 – enable interrupt for timer 5
Bit 12	en4 – enable interrupt for timer 4
Bit 11	en3 – enable interrupt for timer 3
Bit 10	en2 – enable interrupt for timer 2
Bit 9	en1 – enable interrupt for timer 1

10	Word	Timer 0 divisor. Timer 0 operates as a base clock for timers 1 through 6
12	Word	Timer 1 divisor. Continuous timer
14	Word	Timer 2 divisor. Continuous timer
16	Word	Timer 3 divisor. Continuous timer
18	Word	Timer 4 divisor. One-shot timer.
1A	Word	Timer 5 divisor. One-shot timer.
1C	Word	Timer 6 divisor. One-shot timer
1E	Word	Timer 7 divisor. Clock generator for SPI - based on sysclk, not clk0

Interrupts: Int 3 – timer event

SPI (SD-card):

20	SPI register
Read
Bits 7 downto 0: Data received from a single 8-bit SPI transaction with the SD card
Write
Writing to this register triggers an SPI transaction.
The byte written to the lower 8 bits is sent to the SPI device,
and the 8-bit reply to the previous transaction is received
and made available for reading.

22	SPI CS register
Read
Bit 15 Busy – 1 if an SPI transaction is in progress
Write
Bit 0 SD select – 1 for active, 0 for inactive. (inverted with respect to the CS line)

24	Blocking SPI register
Behaves exactly as register 20, except the transaction is delayed (and the cpu
paused) until SPI CS->Busy is low, eliminating the need to poll in software.

100-	SPI Pump registers
These registers are useful for transferring a sector of data from SD card.
Reading waits for SPI CS->Busy to drop, then returns the most recent 16-bits of data.
It also triggers the transfer of a further 16-bits. CPU overhead can thus be kept to
a minimum – it's possible to transfer 64 bytes or more in a single instruction
with judicious use of movem.l.